# AF-6710-32X256-6-RGB-SF Update-Procedure:

- Update Requirements:

  - Test PC with TightVNC viewer installed

- Update Procedure:

  - Connect the test PC LAN port to SBC LAN port 2 (192.168.0.100) or LAN port 1 if address known.

  - Logon to the SBC using the VNC application as follows:

    - Run VNC on the test PC

    - When the connection opens enter the Remote Host IP address.

(Note: test PC must be set up with an IP address within the same domain range as the sign)

    - When the VNC Authentication windows opens enter the password ‘ddisplay’ and click ok.

    - When connected press the windows icon on the top left corner of the VNC window (TightVNC window shown below) to make the windows taskbar visible and close all applications running:

  - Disable the EWF filter as follows:

    - Reboot the SBC (note: the SBC needs to be rebooted before the EWF filter is disabled otherwise the CF card may become corrupt).

    - Reconnect to the SBC using VNC and close all applications.

    - Open the command prompt.

    - Type ewfmgr –all –commitanddisable –live.

    - Wait for the EWF status to disable (it may be necessary to disconnect and reconnect VNC).

    - Close the command prompt window.

  - Change the Firmware temperature threshold as follows:

    - Open windows explorer and navigate to the C:\Ideaager\ILCS2Setup folder.

    - Open the ILCS2_setup.ini file and edit as follows:

thermal_warning = 60

thermal_error = 70

thermal_critical = 75

thermal_warning_level = 100

thermal_critical_level= 50

    - Save and close the file.

    - Navigate to C:/temp/test/RGB_Test-Script, run RGB_Test-Script and select the Display_Test tab

    - Press the Test_Display button – this should open a command prompt window showing responses from the ILCS2 Image controller and the cluster controllers

    - Select the Setup tab and press the Run_Setup button to read in the new temperature threshold settings from the ILCS2_setup file.

    - Press the Send_Configuration buton to load the new settings into the controllers – this will take a few minutes.

    - When the update is complete, press the Restart_Cluster button and wait 1 minute.

    - Press the Restart_ILCS2 button and wait 1 minute.

    - Close the RGB_Test-Script and command prompt windows.

  - Change the Software temperature threshold as follows:

    - Open windows explorer and navigate to the C:\078_DVS_PLAYER_4_2_3_20150529\diagnostics folder.

    - Open the ilcs2gui.properties file and edit as follows:

temperatureHighThreshold=60

    - Save and close the file.

  - Enable the EWF filter:

    - Open the command prompt

    - Type ewfmgr –all –enable

    - Reboot the SBC (note: VNC will logout)

  - Check The EWF filter is enabled:

    - Logon to the SBC with VNC after it has fully restarted.

    - Open the command prompt

    - Type ewfmgr c: and check the status is enabled.

    - Close the command prompt window.